## Slide 1: Siemens-Nixdorf Case, Universität Augsburg,1989
Tiziano Di Gregorio Botek (Snr: 2089304) Alexander Maier (Snr: 2095044)
Paul Toussing (Snr: 2105332) Oskar Weber (Snr: 2100180)

## Slide 2: Content
Introduction
Siemens Solution
Our approach
Preliminary results

## Slide 3
Introduction
Our approach
Siemens Solution
Preliminary Results
Introduction
Drilling: bottleneck process in printed circuit board (PCB) manufacturing
Drilling process time = drilling time + moving time
Different hole diameters and locations for each PCB
2-dimentional Euclidian plane
Notes: 3

## Slide 4
Introduction
Our approach
Siemens Solution
Preliminary Results
Problem definition
Optimization of the production capacity of printed circuit boards (PCBs).
Drilling time: Machine cannot be changed
Moving time: Drilling path can be changed
Provide a solution in less than 5 minutes for any dataset
Notes: 4

## Slide 5
Introduction
Our approach
Siemens Solution
Preliminary Results
Problem definition
The x-axis moves 10% slower than the y-axis
Toolbox located at a fixed place
Variable: movement of the drill head
Notes: 5

## Slide 6
Introduction
Our approach
Siemens Solution
Preliminary Results
Problem Transformation
Optimization of the distance travelled by the drill:
Rescaling of the plane
Total distance define by the sum of Euclidian distance of the going from one point to another
Notes: 6

## Slide 7
Introduction
Our approach
Siemens Solution
Preliminary Results
Model formulation: Travelling salesman problem (1): Objective function
Variables:
: total distance travelled by the drill head
: total number of holes to be drilled
: distance between hole and hole
: binary variable if the path goes from point to
Notes: 7

## Slide 8
Introduction
Our approach
Siemens Solution
Preliminary Results
Model formulation: Travelling salesman problem (2): Constraint
Constrains:
Each hole must be visited exactly once
After drilling at a hole, drill must move to another hole
Starting and ending position at the toolbox (0,0)
Introducing dummy variable to prevent sub-tours:
Variables:
: binary variable if the path goes from point to
: place in the path order of the hole
Notes: 8

## Slide 9
Introduction
Our approach
Siemens Solution
Preliminary Results
Model formulation: Travelling salesman problem (1): Subtours
Auxillary variable:
: place in the path order of the hole
Introducing dummy variable to prevent sub-tours:
Notes: 9

## Slide 10
Introduction
Our approach
Siemens solution
Preliminary Results
Holes drilled in lexicographical order
Total Euclidian Distance:
On re-scaled plane: 142825.1 machine units
Example for one hole size of PCB D
Notes: 10

## Slide 11
Introduction
Siemens Solution
Our approach
Preliminary Results
Linear optimization solution: an example of a better solution
Total Euclidian Distance:
On re-scaled plane: 53344.687 machine units
Highly optimal solution
Within 4.1619% of true optimum
Costly: power and time
Inefficiency
Notes: 11

## Slide 12
Introduction
Siemens Solution
Our approach
Preliminary Results
Solution: investigating heuristics solutions
Trade-off between optimality and time/computation costs
  Cost and time efficiency particularly for many holes
Approximation algorithms:
  Nearest Neighbour algorithm, Greedy algorithm, etc.
Comparison with the lower bound (optimal solution)
Notes: 12

## Slide 13: Questions